DEPARTMENT FOR INFRASTRUCTURE AND TRANSPORT

SOUTH AUSTRALIA

BLACK SPOT PROGRAM GUIDELINES

Issue Date

July 2023

# Document control

# Document Status

| Document Owner: Director, Transport Strategy and Network Planning |
| --- |
| Action | Name and Position | Doc. KNet Reference | Version |
| Prepared By: | Amit Dua Sen. Road Safety Network Engineer | #20246106 | V1 |
| Reviewed and Approved by: | Fiona Cartwright Manager Road Network Planning | #20246106 | V1 |
| Document Review Schedule: As required |

TABLE OF CONTENTS

Document control	1

Document Status	1

1	PURPOSE	1

2	BACKGROUND	1

3	safe system approach	1

4	ROLES	2

4.1	Geographic Definitions	2

4.2	Projects on Local Roads	2

5	ELIGIBLE ROAD SAFETY WORKS	3

5.1	General	3

5.2	Eligibility Criteria	4

5.2.1	Location and Extent	4

5.2.2	Crash and Safety Considerations	4

5.2.3	Benefit Cost Ratios	4

5.3	Safe System Principles Considerations	4

5.4	Staged Construction	5

5.5	Costs	5

5.6	Performance	5

6	PROJECT NOMINATIONS	6

6.1	Nominations	6

6.2	Call for Nominations	7

6.3	Closing Date for Nominations	7

7	APPROVAL PROCESS – ROAD SAFETY PROJECTS	8

7.1	Assessment of Nominations	8

7.2	Program Approval	8

8	INFORMATION AND RECOGNITION	9

8.1	Funding Deed	9

8.2	Reporting	9

8.3	Payments to Councils	9

8.4	Project Signage	9

8.5	Information Contact	9

APPENDIX A – Black Spot Criteria	10

APPENDIX b – DEVELOPMENT OF black spot PROGRAM (SA roads)	13

APPENDIX C – PROJECT SIGNage	15

# PURPOSE

These guidelines provide information on the administration and operation of the Australian Government Black Spot Program. The guidelines provide guidance on project eligibility, the project nomination, assessment and prioritisation process and project reporting requirements.

# BACKGROUND

Road safety infrastructure programs are aimed at bringing about significant reductions in serious road casualties by the identification and treatment of locations and sections of road that have a poor casualty crash record or that have a significant crash potential identified by safety audits.

# safe system approach

The program is focussed on the most effective treatments that can be applied to the key crash types, consistent with Safe System principles. The Safe System approach to road safety is built on several key principles:

Human Factors

- No matter how well we are trained and educated about responsible road use, people make mistakes, and the road transport system needs to accommodate this.

Human Frailty

- The finite capacity of the human body to withstand physical force before a serious injury or fatality can be expected is a core system design consideration.

Forgiving Systems

- Roads that we travel on, vehicles we travel in, speeds we travel at, and communities we live in, need to be more forgiving of human error.

Shared Responsibility

- Everyone has a responsibility to use the road safely and organisations, businesses and communities have a responsibility to design, manage and encourage safe use of the road transport system.

The department (DIT) reserves the right to deem the project ineligible should a nominated project be deemed to not align with Safe System principles. If clarification is required relating to Safe System treatments, Councils can contact DIT.SABlackspots@sa.gov.au .

# ROLES

The Commonwealth Department of Infrastructure, Transport, Regional Development and Communications and the Arts is responsible for administering and setting the eligibility criteria for the Australian Government Black Spot Program.

The department (DIT) is responsible for:

- Setting broad road safety policy and strategy

- Seeking the necessary program approvals

- Coordinating the development of Annual Program for road safety improvements including the seeking of nominations

- Checking of submissions, and

- Prioritisation of projects in line with these guidelines.

It is the responsibility of Councils, DIT, organisations and individuals to submit project nominations in line with these guidelines.

The Australian Government Infrastructure Investment Black Spot Program is subject to approval by the Federal Minister for Infrastructure, Transport and Regional Development.

## Geographic Definitions

This program distinguishes between Greater Urban and Rural Area boundaries. The boundaries are based on the Adelaide Statistical Division Map.

The Greater Urban Area is defined as the Adelaide metropolitan area including all of Mount Barker and Adelaide Hills LGAs in the east, Gawler and areas of the Barossa, Light and Mallala LGAs in the north and all of Onkaparinga LGA in the south. Rural is defined as being outside of the Adelaide Statistical Division.

A map is provided on the website http://dit.sa.gov.au/blackspot.

## Projects on Local Roads

The maximum project cost for individual Council projects on local and state roads is $2.0 million and the minimum project cost is $20,000 and is fully funded under the Australian Government Black Spot Program.

Council nominated projects on either state or local roads that are greater than or equal to $150,000 are required to provide more detailed information (as outlined in the nomination form). The DIT Estimating Manual, link: https://www.dit.sa.gov.au/__data/assets/pdf_file/0003/173532/Estimating_Manual.pdf can be used by council as a guide for developing project estimates.

Projects nominated by Council on state roads shall be supported by the relevant DIT section such as Road Maintenance Zone and Traffic Integrity, as well as all concept plans and estimates developed in accordance with DIT standards and estimating manual, prior to the project nomination.

Other considerations

Project nominations on strategically important DIT arterial roads or on signalised intersections, will also take traffic efficiency impacts into consideration. This is to ensure that projects do not create significant traffic flow or congestion problems, or create potential for other safety issues or additional changes to road infrastructure.

# ELIGIBLE ROAD SAFETY WORKS

## General

The Australian Government Black Spot Program is available for safety improvement works on the state arterial roads and council roads.

Under the Australian Government Black Spot Program, eligible nominations on national highways can be submitted. These must not duplicate projects submitted or funded under other Australian Government National Roads programs.

Eligible road safety works are those designed to treat sites with a recorded history of casualty crashes in accordance with the eligibility criteria.

Sites that do not meet the crash history criteria but have been the subject of an official road safety audit are eligible.

Eligible works include:

- Safety improvement works and traffic control devices including traffic signals

- Work on adjacent road environments – e.g. hazard protection works

- Safety improvement works that may include speed reduction treatments as part of the treatment.

Ineligible works are:

- Purchase of road building plant and equipment

- Purchase of law enforcing equipment such as speed and red light cameras

- Maintenance activities

- Area, network or route based speed treatments.

## Eligibility Criteria

The table in Appendix A summarises Black Spot Criteria explained in more detail in this section.

### Location and Extent

For discrete sites (e.g. an intersection, mid-block or short road section less than 
3 km), the minimum eligibility criteria is a history of at least three (3) reported casualty crashes in the last five years at the site.

For road lengths >= 3 km, the minimum eligibility criterion is an average of 0.20 casualty crashes per kilometre per annum over the length in question measured over five years or the length must be amongst the top 10% of sites identified in the State which have an identified higher crash rate than other roads.

### Crash and Safety Considerations

Measures of casualty crashes should be provided from the most recently available five-year period, 2017-21 for 2023-24 program.

For works recommended by an official Road Safety Audit Report, the report must have been undertaken by an Accredited Road Safety Auditor.

### Benefit Cost Ratios

The Benefit Cost Ratio (BCR) must be greater than or equal to 2.0, for reactive projects.

A discount rate of 7% shall be applied in the calculation of the BCR. Additional guidance on BCR calculations and crash reduction factors are available on the DIT Black Spot website (http://dit.sa.gov.au/blackspot).

For BCR calculation purposes either of the two following methods can be used and whichever provides the highest benefit can be quoted.

- BITRE costs method (crash cost based on severity)

- Austroads costs method (crash cost based on crash type).

## Safe System Principles Considerations

Concept development and scoping of the nomination should consider Safe System principles - including issues such as different road users, vulnerable road users, creating a more forgiving road treatment or environment and safer speed environments.

Safe System principles should be considered where feasible in the project scope prior to nomination.

## Staged Construction

Complex projects should be submitted on the basis of delivery and funding over a two year period. Eligibility criteria apply to the project as a whole.

These are projects where a detailed design needs approval of an authority or where land acquisition, service relocations or availability of contractors necessitate longer project duration.

In such cases, the nomination should detail the staging and the required funding and scope of works for each year must be stipulated.

Projects that have not commenced in the first year of funding will be reviewed to determine if the project is still feasible or recommended for withdrawal or deferral.

## Costs

All costs directly associated with a project are eligible for funding. The following costs cannot be claimed as part of project costs:

- Administrative overheads and other indirect costs

- Cost incurred after installation i.e. operating and running costs

- Purchase of road building plant and equipment

- Purchase of law enforcement equipment such as speed and red light cameras

- Costs involved in undertaking Road Safety Audits

- Costs involved in preparation of nominations.

## 5.6	Performance

Recent years have seen increased interest in the Black Spot program. However, risk of annual under-expenditure for new road projects through project withdrawals or under-expenditure remains a concern. Previous performance in management, communication and delivery of projects to budget and timeline will be considered in the assessment of projects.

# PROJECT NOMINATIONS

## Nominations

DIT shall invite nominations for projects from:

- Local Councils

- DIT

- Various other organisations or the public having an interest in road safety.

Nominations must be forwarded, using the nomination form and relevant supporting documentation, to DIT by the closing date.

Nominations from Councils and DIT must be endorsed by the Chief Executive Officer (Councils) or relevant Zone Delivery Manager (DIT), (in case there is any impact on traffic flow, a nomination must be endorsed by Manager Traffic Integrity (DIT)) and include:

- Details of the crash history – (to be included in the BCR calculation spreadsheet)

- The proposed treatment including sufficient details and drawings for accurate cost estimating and to clearly show what is proposed

- An accurate cost estimate, including clear identification of risk/contingency factors and time schedule

- All DIT project nominations must provide a copy of a registered estimate

- Local Government project nominations greater than or equal to $150,000 must provide a copy of detailed cost estimate or the DIT Estimating Manual can be used as a guide for developing project estimates, as well as any additional information (as per the nomination form)

- The Benefit to Cost Ratio calculation for reactive projects

- A copy of the Road Safety Audit Report for proactive project nominations

- Any other information that contributes to the details and justification of a project

- If works impact DIT’s roads, Councils must contact DIT’s relevant office to obtain approval in principle and attach supporting correspondence to the nomination

- Project nominations by Council on state roads shall be supported by the Asset Engineer and Manager Traffic Integrity of DIT, as well as all concept plans and estimates developed in accordance with DIT standards and estimating manual, prior to the project nomination

- For any nominations involving speed reduction as part of a treatment, Councils shall contact DIT Traffic Services to obtain approval in principle and attach supporting correspondence to the nomination. Such proposals will need to demonstrate compliance with DIT speed limit standards and guidelines.

Any nomination that is proposed from someone other than Council or DIT shall be supported by the relevant Road Manager responsible for the care, control and management to ensure it meets program criteria and then referred to the relevant Council or DIT Manager Traffic Integrity and Road Maintenance Delivery Zone Manager to endorse the nomination, if applicable.

Applications not supported by the relevant Road Manager/s will be considered ineligible.

## Call for Nominations

Project nominations will be sought from July through to October for the following financial year.

At the time of call, DIT will provide supporting documentation in the form of nomination forms, BCR pro forma and crash reduction factors to be applied in assessment of projects. Supporting information including crash maps will be available from the website.

Any cost variation must be contained within the overall project and program budget. Project estimates must therefore be accurate to ensure delivery of the program without having to defer projects.

Each nomination is to be submitted separately, if more than one nomination is being submitted.

Nominations are to be submitted as follows:

- One original submitted by post

Australian Government Blackspot Program SA Nominations

Att: Ty Edwards

Road Safety Network Engineer

Road Network Planning

Transport Strategy and Planning Division

Department for Infrastructure and Transport

GPO Box 1533

ADELAIDE SA 5001

OR

- One electronic copy submitted by email

DIT.SABlackspots@sa.gov.au

Subject: ‘AGBS Program SA Nominations - [insert road location]’

## Closing Date for Nominations

The closing date for nominations will be as specified in the letter calling for nominations and as published on the website http://dit.sa.gov.au/blackspot .

Late or incomplete nominations will not be accepted.

# APPROVAL PROCESS – ROAD SAFETY PROJECTS

## Assessment of Nominations

DIT will assess nominations for completeness and accuracy in accordance with these guidelines. Where necessary, DIT shall consult with the nominees directly.  Nominations that fail to meet the eligibility criteria or are not supported by an official Road Safety Audit Report or have insufficient information provided will not be considered.

Upon completion of the assessment, projects nominated based on crash criteria are ranked by their BCR. Proactive projects supported by an official Road Safety Audit Report are ranked by their Risk Reduction Cost Ratio obtained from ARRB’s Road Safety Risk Manager.

## Program Approval

The South Australian Black Spot Consultative Panel meets to recommend approval of eligible nominations for the Australian Government Black Spot Program, within the funding available.

Appendix B shows the development of the Black Spot Program for South Australian Roads.

# INFORMATION AND RECOGNITION

## Funding Deed

Councils successful in obtaining funding are required to enter into a funding deed with DIT. This deed outlines funding arrangements, project details, conditions and reporting requirements.

## Reporting

Councils are required to provide DIT with regular progress reports on approved projects including advice of the commencement and completion dates. These reports are required to be submitted to DIT in accordance with a reporting schedule which will be advised within the funding deed upon project approval.

## Payments to Councils

Payments to Councils will be made on the basis of progress claims submitted to DIT for completed stages of projects or as otherwise specified in the funding deed.  Council payment claims are to be submitted to the DIT Liaison Officer for processing, as outlined in the funding deed.

## Project Signage

The road authority for the approved project shall erect signs on each road approach at the site of the project. The signs shall conform to the design shown in Appendix C and shall remain in place for one year after the completion of works. The initial cost of the signs can be charged to the cost of the project.

Signs for Australian Government funded Black Spot projects shall comply with the ‘Notes on Administration’ requirements.

## Information Contact

Any enquiries about the Black Spot program should be directed to the email address DIT.SABlackspots@sa.gov.au   or contact Mr. Ty Edwards, Road Safety Network Engineer on 08 7133 2893.

# APPENDIX A – Black Spot Criteria

|  | Australian Government |
| --- | --- |
| Who can nominate | Councils, DIT (the department), organisations and individuals |
| Eligible Roads | National Highways, State and Local Roads |
| Endorsement of Recommended Projects | Australian Government - SA Consultative Black Spot Panel |
| Funding & Project Cost Criteria |
| Program Funding | 100% Australian Government funded |
| Contributions to Project Cost | Yes – encouraged |
| Funding Distribution Metro / Rural | Approximately 50:50 |
| Reactive Projects Proactive Projects | Up to 100% reactive projects (BCR ≥ 2.0) Up to 30% proactive projects (no minimum BCR, however Road Safety Audit required) |
| Maximum funding contribution towards Project Cost | $2,000,000 (DIT and Council Nominations) |
| Minimum Project Cost | $20,000 |
| Cost Estimate requirements | Registered DIT estimate required for all DIT projects Detailed cost estimate required for Local Government projects >= $150,000 – refer nomination form and DIT Estimating Manual |
| Eligible Costs | All direct costs including capital and design costs |
| Ineligible Costs | Purchase of road-building plant or equipment / Costs involved in the preparation of Road Safety Audits / Maintenance costs; and Costs incurred after installation |

|  | Australian Government |
| --- | --- |
| Crash Criteria |
| Intersection or Mid-Block (< 3km) | 3 casualty crashes in the last 5 years |
| Road Length (≥ 3km) | 0.20 crashes/km/year over last 5 years |
| Crash Period | Recent 5 years (i.e. From 2018 to 2022 for 2024-2025 program) |
| Benefit – Cost Ratio (BCR) using either BITRE costs method or Austroads costs method, whichever is higher | ≥ 2.0 |
| Discount Rate | 7% |
| Crash Reduction Factors | From Australian Government Black Spot Notes on Administration and DIT BCR calculation spreadsheet |
| Prioritisation (Reactive Projects) | Based on BCRs using BITRE methodology or Austroads crash type costs method |
| Prioritisation (Proactive Projects) | Based on ARRB Risk Reduction Cost Ratio |
| Proactive projects | Require a Road Safety Audit |

|  | Australian Government |
| --- | --- |
| Project Delivery |
| Funding Deed needed between Council and DIT | Yes |
| Time Frame | Project to be completed within the financial year unless approved as specified in Funding Deed |
| Approvals | Design and technical approvals from DIT for works on National and State Roads, Environment, Heritage and Aboriginal clearances where required |
| Project Signs | Yes, for projects value: < $100,000 – temporary signage during construction ≥ $100,000 – permanent signage during the construction and one year after construction |
| Reporting | Status reporting as specified Variation Form - in case of variations to scope and/or cost Project Completion Report, and As specified in Deed or other correspondence |
| Recognition | All media releases to acknowledge that funding is from Australian Government Australian Government approves media releases |

# APPENDIX b – DEVELOPMENT OF black spot PROGRAM (SA roads)

# APPENDIX C – PROJECT SIGNage

Australian Government Black Spot Sites

Signs erected at approved Australian Government Black Spot sites must comply with the Department of Infrastructure, Regional Development and Cities’ Signage Guidelines located under Black Spot Program. This is available on the Australian Government Black Spot website:

https://investment.infrastructure.gov.au/files/signage_guidelines/BOF-signage-guidelines.pdf

# Footnotes

NOTE: REGISTERED ESTIMATE REQUIREMENTS IN LINE WITH DIT ESTIMATING MANUAL

# Text boxes

Identify Problem Location and access crash data & Location

1. Australian Government funding is available for National Highways, State and Local roads.

2. Detailed crash information can be obtained from DITI’s Crash Unit or black spot website.

3. Check Australian Government Black Spot Notes on Administration for eligibility criteria.

4. Undertake a Road Safety Audit by an accredited auditor.

5. The cost of countermeasure must include all design, construction, project management associated costs.

6. Benefit Cost Ratio (BCR) must be calculated as per the guidelines to calculate BCRs and using crash reduction matrix.

7. Risk Reduction Cost Ratio (RRCP) must be calculated using ARRB’s Road Safety Risk Manager (if available).

8. Project nominations by Council on DIT roads shall be supported by the relevant DIT section, as well as all concept plans and estimates developed in accordance with DIT standards and estimating manual, prior to the project nomination.

9. Complete nomination form and attach:

- Crash Data

- Proposed concept scheme

- Road safety audit and RRCR or BCR Calculation

- Other supporting documentation

NO

Undertake a Road Safety Audit (RSA)

Is the Black Spot Crash criteria met?

YES

Determine cost of countermeasures and Benefit Cost Ratio (BCR) or Risk Reduction Cost Ratio (RRCR)

Is the nomination, supported by the relevant Road Authority?

NO

YES

Does it meet the Cost Eligibility Criteria?

NO

Ineligible for Black Spot funding

YES

Eligible for Australian Government

Funding

Is BCR >2, or is a RSA provided?

NO

YES

NO